Laboratory Biosafety Compliance Inspection Checklist

Biosafety Level 3

Note:  Also refer to the Compliance Inspection Checklist for Biosafety Level 2.

Date   ______________			Laboratory Location  __________________

Responsible Individual  ________________

IBC#  _________________________	Person Interviewed ____________________

Title ___________________________________________________________________ _______________________________________________________________________

Queries are based on Appendix G of the NIH Guidelines and the Biosafety Level 3 Section of the Biosafety in Microbiological and Biomedical Laboratories, 5th Edition, 2007

Abbreviations: NA, not applicable; PPE, personal protective equipment; PI, primary investigator.

.

(Note: All BL-1 and BL-2 practices are followed in BL-3 containment laboratories.)

Circle the response that best describes the laboratory in which work will be performed.

| A. Standard Microbiological Procedures |  |
| --- | --- |
| 1. Persons under 16 years of age are not allowed to enter the laboratory. | Yes, No |
| 2. Concurrent experiments involving BL-2 and BL-3 containment are conducted in accordance with all BL-3 level laboratory practices. | Yes, No |
| 3. Personnel are advised by the PI of special hazards associated with the agents(s) utilized. | Yes, No |
| 4. Personnel are required to follow the practices and procedures outlined in the BL-3 Biosafety Manual for high-level containment. | Yes, No |

| B. Special Practices |  |
| --- | --- |
| 1. The Director for each ABSL-3/BSL-3 laboratory restricts access to personnel whose presence is required for program or support purposes. | Yes, No |
| 2. All personnel working at BL-3 containment have demonstrated proficiency in standard microbiological practices and techniques before work with risk group-3 agents commences. | Yes, No |
| 3. All manipulations involving biohazardous materials are conducted in a biosafety cabinet within the containment module. | Yes, No |
| 4. A biological spill emergency plan for BL-3 containment is posted in the laboratory. | Yes, No |
| 5. Entrance and exit procedures are posted in the BL-3 laboratory suite. | Yes, No |
| 6. Each containment module has posted a biohazard warning sign which identifies the biohazardous agent present, the name and emergency contact information for individual(s) utilizing the containment module, and any special requirements for entering the area. | Yes, No |
| 7. The work surface of the biosafety cabinet and other containment equipment are decontaminated when work with the biohazardous agent is finished. | Yes, No |
| 8. All waste is appropriately decontaminated before removal from the BL-3 laboratory. | Yes, No |
| 9. An Institutional policy describing the collection and storage of serum samples from at risk personnel is available and followed. | Yes, No |
| C. Safety Equipment (Primary Barriers and PPE) |  |
| 1. Personal protective equipment to include a solid-front or wrap-around gown, shoe covers, and gloves are worn by all workers when accessing the BL-3 laboratory and removed prior to exiting the laboratory. | Yes, No |
| 2. Reusable clothing is decontaminated with an appropriate method before being removed from the containment suite. | Yes, No |
| 3. The biosafety cabinet is located away from the door, from the room air supply louvers, and from heavily-traveled laboratory areas. | Yes, No |
| 4. Respiratory protection is worn by all personnel entering the ABSL-3/BSL-3 suite. | Yes, No |
| 5. Aerosol producing equipment is contained in devices that exhaust air through HEPA filters before discharge into the laboratory. If yes: A method is available to monitor the HEPA filters for replacement. | Yes, No Yes, No |
| D. Laboratory Facilities (Secondary barriers/Engineering controls) |  |
| (These are evaluated annually by the Biosafety Officer using a re-certification process checklist. A copy of this checklist is available from the Safety and Security Manager for each containment laboratory.) |  |